## Slide 1
Radiation Effects Project 2
Physics-lecture version: slides as a compact summary of the physics notes and roadmap
1
Radiation-Induced Defect Evolution and Device Degradation in Silicon
Goal:
build a physics-based chain from radiation deposition → defect creation and evolution → field change → carrier-transport change → device degradation
This deck is organized as a lecture:
• governing equations
• physical interpretation
• module-to-module coupling
• verification logic
Place your custom physics schematic here
Key point: Treat the project as one connected physical story, not as isolated code modules.

## Slide 2
Project physics chain
What the full framework is trying to explain
2
Causal sequence
Why each step matters
1. Radiation deposits energy in silicon.
2. Deposited energy seeds point defects and effective defect populations.
3. Defects diffuse, react, cluster, dissociate, and anneal.
4. Charged defects modify the space-charge density.
5. The electrostatic field and temperature field change carrier motion.
6. Carrier transport and recombination change measurable device behavior.
Damage is not only about where energy was initially deposited.
The later evolution matters because the material keeps changing after the radiation event.
Temperature is active physics, not a bookkeeping variable: it changes diffusion coefficients, annealing rates, mobility, and recombination.
The final quantity of interest is device degradation, so the framework must connect materials physics to electronic behavior.
Key point: A deposition map is only the beginning; the project is about the downstream evolution of that damage.

## Slide 3
Roadmap and run order
How the modules fit together in the intended workflow
3
Full workflow
Module 1 → Module 3 → Module 4a / 4b → Module 2 → Module 5 → Module 6 → Module 7
Module 1: interaction-resolved Geant4 radiation deposition campaign
Module 3: 2D defect evolution with diffusion, reaction, and annealing
Module 4a: continuum thermal transport baseline
Module 4b: phonon-aware thermal comparison branch
Module 2: 2D electrostatics with defect-dependent space charge
Module 5: 2D drift-diffusion carrier transport with defect-assisted recombination
Module 6: self-consistent multiphysics iteration
Module 7: extrapolation to larger scales and rarer events
Key point: The project is built to move from an externally imposed radiation insult to a self-consistent degraded device state.

## Slide 4
Architecture decisions behind Project 2
Why the revision moved to 2D and split the thermal module
4
Why 2D for Modules 2–6
Why split Module 4 into 4a and 4b
A 1D model suppresses lateral spreading, field bending, localized heating, and current crowding.
A Geant4 deposition pattern is naturally spatially structured, so the downstream modules should preserve that structure.
The first 2D implementations can still stay simple: rectangular domains, structured grids, simple boundary conditions, and weak coupling.
Module 4a is the baseline continuum heat-equation model.
Module 4b is the richer phonon-aware branch for cases where bulk conductivity is not enough.
This split lets the project compare a simpler thermal model against a more physically detailed one instead of assuming the richer model is always necessary.
Key point: The revision is not complexity for its own sake; it preserves the spatial physics that matter while keeping the first implementation executable.

## Slide 5
Module 2: electrostatics starts from Gauss's law
Physics note summary: from Maxwell to the Poisson problem
5
In the electrostatic limit, the magnetic time-variation terms drop out and the problem reduces to the scalar electric potential.
With E = −∇φ and ∇·E = ρ/ε, the governing equation becomes a Poisson equation for φ.
This is the natural equation because the local curvature of φ is determined by the local space-charge density.
Core electrostatic chain
∇ · E = ρ / ε
E = − ∇φ
⇒ ∇ · ( ε ∇φ ) = − ρ
Uniform-permittivity limit
ε ∇²φ = − ρ
or ∇²φ = − ρ / ε
Key point: Module 2 is fundamentally a space-charge-to-potential map.

## Slide 6
Module 2: what makes up the semiconductor space charge?
The electrostatic source term is a sum of mobile, dopant, and defect charges
6
The net charge density is not one thing; it is a sum of all charged constituents in the semiconductor.
Electrons and holes contribute mobile charge.
Ionized donors and acceptors contribute fixed dopant charge.
Radiation-induced defects contribute additional charged states and can perturb depletion structure and field profiles.
Charge-density decomposition
ρ = q ( p − n + N_D^+ − N_A^- + Σ_j z_j C_j )
Project 2D Poisson equation
∂/∂x ( ε ∂φ/∂x ) + ∂/∂y ( ε ∂φ/∂y ) = − ρ(x,y)
Key point: Defect physics enters Module 2 by changing the source term ρ(x,y), not by replacing electrostatics.

## Slide 7
Module 2: boundary conditions, coupling, and verification
What must be prescribed, what is received, and what is checked
7
Boundary conditions
Coupling and verification
Dirichlet: prescribe φ at a contact or biased boundary.
Neumann: prescribe normal electric flux, equivalent to surface charge or insulated symmetry conditions.
Mixed physical picture: contacts may be Dirichlet, symmetry planes often Neumann.
Input from Module 3: charged defect populations C_j(x,y,t).
Input from Module 4: temperature-dependent quantities if permittivity or occupations are later made temperature-sensitive.
Output to Module 5: electric potential φ and field E = −∇φ.
Verification cases: zero charge, linear potential, uniform space charge, and a defect-charge perturbation test.
Key point: Module 2 is only as good as the defect populations and boundary conditions that feed it.

## Slide 8
Module 3: defect evolution begins with a conservation law
Physics note summary: balance law + Fick transport + reaction kinetics
8
The state variable is a continuum defect concentration C(x,y,t).
Conservation says the time-rate of change equals inflow/outflow plus local sources and sinks.
Diffusion arises because defects drift down a concentration gradient.
Annealing and reactions are represented by sink/source terms.
Balance-law form
∂C/∂t + ∇ · J = R
With Fick transport and first-order annealing
J = − D ∇C
∂C/∂t = ∇ · ( D ∇C ) − k C + S
Key point: Module 3 is the engine that turns initial damage into a time-evolving defect landscape.

## Slide 9
Module 3: timescales and Arrhenius physics
How to think physically about diffusion versus annealing
9
Characteristic timescales
Thermal activation
Diffusion timescale: τ_D ~ L² / D.
Annealing timescale: τ_A ~ 1 / k.
If τ_D << τ_A, defects spread before they disappear.
If τ_A << τ_D, defects anneal locally before much migration occurs.
Arrhenius reduced coefficients
D(T) = D_0 exp( − E_D / k_B T )
k(T) = k_0 exp( − E_A / k_B T )
The exponential appears because migration and annealing must overcome activation barriers.
In the current reduced model, these are effective coefficients that compress richer microscopic physics into executable continuum parameters.
Key point: Temperature changes the kinetics exponentially, so thermal physics strongly feeds back on defect evolution.

## Slide 10
Module 3: what is implemented now, and how it is checked
From the physics note to the current MATLAB solver
10
The current implementation uses a 2D diffusion-reaction solver with material-aware reduced kinetic coefficients.
The coefficient hierarchy allows dependence on temperature, charge state, dopants, and electric field, while keeping the first implementation numerically manageable.
Geant4 damage maps can be imported as initial defect fields or source terms.
Verification logic from the note:
  pure annealing with no diffusion
  pure diffusion with no reaction
  uniform-state preservation
These checks verify conservation structure, kinetics, and the numerical diffusion operator separately.
Key point: Module 3 is already the clearest bridge from Geant4 outputs to later electrical and thermal consequences.

## Slide 11
Module 4a: continuum thermal transport from energy conservation
Physics note summary: internal-energy balance + Fourier law
11
Temperature is introduced through local conservation of energy in a material element.
The internal-energy change is driven by heat-flux divergence and local volumetric sources.
Fourier's law closes the problem by relating heat flux to the temperature gradient.
Energy conservation + constitutive law
ρ c_p ∂T/∂t = − ∇ · q + Q
q = − k ∇T
Transient heat equation
ρ c_p ∂T/∂t = ∇ · ( k ∇T ) + Q
or ∂T/∂t = α ∇²T + Q/(ρ c_p)
Key point: Module 4a supplies the baseline temperature field that later updates defect and transport coefficients.

## Slide 12
Module 4a: physical interpretation of the heat equation
What each term means for radiation-damaged silicon
12
What can act as a heat source?
Boundary conditions and scales
Deposited radiation energy can appear as an initial or transient source.
Electrical power dissipation can heat the device during operation.
Defect reactions may also contribute weak heating or cooling terms in later refinements.
Dirichlet: fixed temperature boundary.
Neumann: fixed heat flux or adiabatic boundary.
Robin: convective or interfacial thermal exchange.
The thermal diffusion timescale is τ_th ~ L² / α, which determines how fast a local hot spot spreads.
Key point: Module 4a is the first thermal baseline because it is simple, physically interpretable, and fast to verify.

## Slide 13
Module 4a: coupling back into defect physics
How the temperature field enters Module 3 and why verification is straightforward
13
The main role of Module 4a is not just to predict T(x,y,t), but to update temperature-dependent coefficients elsewhere.
In Module 3, both the defect diffusivity D(T) and annealing rate k(T) can be updated from the thermal field.
Later, temperature can also enter mobility, recombination, and carrier statistics in Module 5.
Thermal-to-defect coupling
D = D(T)
k = k(T)
Verification cases in the note:
  uniform equilibrium
  localized hot-spot diffusion
  driven steady-source case
Key point: Without Module 4a, defect evolution is missing one of its strongest physical control knobs.

## Slide 14
Module 4b: why a plain continuum thermal model can become insufficient
Physics note summary: in crystalline silicon, heat is carried by phonons
14
Fourier's law assumes a local constitutive relation with an effective bulk conductivity.
That can break down when defect scattering, boundary scattering, size effects, or nonequilibrium phonon transport become important.
In silicon, the natural microscopic heat carriers are phonons, so a richer model should talk about phonon distributions and scattering.
Microscopic starting point
∂f/∂t + v_g · ∇_r f = ( ∂f/∂t )_coll
Here f is the phonon distribution function and the collision term encodes scattering.
Module 4b keeps this microscopic logic while still aiming for a reduced executable PDE.
Key point: Module 4b exists to capture physics that a single bulk conductivity k cannot.

## Slide 15
Module 4b: reduced phonon-aware thermal transport model
From phonon scattering logic to a defect-dependent conductivity
15
A practical reduced model is to let the conductivity depend on defect concentration, temperature, or both.
This is motivated by phonon-defect scattering: more defects shorten the phonon mean free path and reduce thermal conductivity.
The PDE can still resemble the heat equation, but the physics inside k is richer.
Defect-aware conductivity idea
k = k(T, C_d, ... )
Module 4b governing form
ρ c_p ∂T/∂t = ∇ · [ k(T, C_d, ...) ∇T ] + Q
Key point: Module 4b may look mathematically similar to Module 4a, but it is physically different because the conductivity itself becomes part of the damage physics.

## Slide 16
Module 4a versus Module 4b
What should be compared, and when should 4b outperform 4a?
16
When 4b is expected to matter
Comparison strategy
High defect densities that materially change phonon scattering.
Strong local gradients or small geometric features where bulk-like heat flow becomes questionable.
Cases where a constant or weakly varying conductivity fails to reproduce the measured or simulated thermal response.
Compare temperature peaks, lateral spreading rates, relaxation times, and the resulting impact on D(T) and k(T) in Module 3.
The point is not only to compare temperatures, but also to compare downstream defect-evolution consequences.
Key point: Module 4b is justified only if the richer thermal physics changes the defect and device predictions in a meaningful way.

## Slide 17
Module 5: carrier transport under a damaged field and trap landscape
Planned physics summary from the roadmap
17
Once the defect state and electrostatic field are known, the next question is device behavior.
Electrons and holes move by drift in the electric field and diffusion down concentration gradients.
Defects also act as traps and recombination centers, so radiation damage affects not only fields but carrier lifetimes and transport pathways.
Carrier-current picture
J_n = q μ_n n E + q D_n ∇n
J_p = q μ_p p E − q D_p ∇p
Continuity with generation/recombination
∂n/∂t = (1/q) ∇ · J_n + G − R
∂p/∂t = −(1/q) ∇ · J_p + G − R
Key point: Module 5 is where the materials physics becomes an electrical-performance prediction.

## Slide 18
Module 6: coupled multiphysics degradation model
Why the modules cannot remain independent forever
18
In the final framework, Modules 2, 3, 4a/4b, and 5 must be iterated to consistency.
Defects modify space charge and recombination.
Temperature modifies defect kinetics and transport coefficients.
Carrier transport can create additional Joule heating and alter occupations.
Coupled unknowns
{ C_j(x,y,t), T(x,y,t), φ(x,y,t), n(x,y,t), p(x,y,t) }
A practical strategy is weak one-way coupling first, then stronger feedback, and finally iterative convergence to a chosen tolerance.
This makes the multiphysics executable without pretending the fully coupled problem is easy on day one.
Key point: Module 6 is the point where the project becomes a real degradation simulator rather than a set of separate solvers.

## Slide 19
Module 7: multiscale extrapolation and scalable prediction
How to move beyond what a direct high-fidelity solve can afford
19
Direct high-fidelity simulation will always be limited in spatial extent, time horizon, or event statistics.
Module 7 exists to push beyond those limits using controlled approximations rather than uncontrolled guesses.
Candidate strategies include reduced-order models, statistical upscaling, surrogate models, hybrid multiresolution workflows, and quantified error bars.
This module is especially important if the project is eventually used to predict rare-event degradation or large-area device behavior.
Key point: Module 7 is what turns a physically rich simulator into a practically useful prediction tool.

## Slide 20
Conclusion and immediate presentation strategy
What this lecture-style deck is trying to communicate
20
Main scientific message
What to emphasize during the talk
Radiation damage in silicon is a dynamic, coupled, multiphysics problem.
The project is designed to connect initial radiation deposition to measurable device degradation through explicit intermediate physics.
The existing physics notes already define the backbone for Modules 2, 3, 4a, and 4b.
Use your custom drawings to show the physical picture, not to replace the equations.
Treat each slide as one derivation step or one physical idea.
For a 30-minute talk, this 20-slide version is a build draft; later trim by merging slides within each module.
Key point: The strongest framing is: radiation creates evolving material damage, and evolving material damage changes device behavior.